## Slide 1: 16-Steps Sequencer and Synthesizer
Zhuowen Lin & Jinyue Guo
11510818 & 11510478
Information Engineering, SUSTech

## Slide 2: Speech Outline
Inputs & Outputs
Components of the circuit
Result demonstration
Further enhancements

## Slide 3: Inputs & Outputs

## Slide 4: Inputs
Switches
  Each of the 16 switches is assigned to a note at a specific time.
  When the time passes it, a note of the selected frequency will play.
Buttons
  BTNR: Save: assign any switch that is in the on position with the current frequency.
  BTNU: Switch frequency: rotate through the 16 frequencies.
  BTNC: Play/Pause
  BTNL: Reset: erase all assigned tones.

## Slide 5: Outputs
LEDs
  LEDs above each switch.
  Light up when a tone is playing on that particular switch.
Seven Segment Display
  Show which frequency is being worked with.
  Rotate from 0 to F.
Speaker
  Sound wave at different frequencies.

## Slide 6: Components of the Circuit

## Slide 7: Button Toggle – Play & Pause
FSM
  Toggle between two states exactly one time when the button is pressed

## Slide 8: Button Debouncer
Button bounce
  Switch between states in FSM
Debouncer
  By Scott Larson of Digi-key
  10.5 ms stable input time

## Slide 9: Clock Dividor – BPM setting
Convert 100 MHz to lower frequencies
  Used to set BPM

## Slide 10: Counter – Tone / Switch Tracker
Keep track of the tone
  Speaker knows which tone to be played
  Seven segment display knows which number to be displayed
Keep track of the switch
  Speaker knows which switch position to be played
  Counter increasing speed: BPM
T flip-flop
  4 bits  4 T flip-flops
  Least significant bit: toggle each time
  The other bits: toggle when all of bits below them are equal to one.

## Slide 11: D Flip-Flop
Remember the tone of 16 switches

## Slide 12: Seven Segment Display
Course Lab 3
  Hexadecimal number

## Slide 13: Square Wave Generator
Change frequency dividing factor
Number | Tone | Max Count
0 | 0 | 0
1 | a | 227272
2 | c1 | 191114
3 | d1 | 170262
4 | e1 | 150372
5 | g1 | 127552
6 | a1 | 113636
7 | c2 | 95556
Number | Tone | Max Count
8 | d2 | 85131
9 | e2 | 75843
10 | g2 | 63776
11 | a2 | 56818
12 | c3 | 47778
13 | d3 | 42566
14 | e3 | 37922
15 | g3 | 31888

## Slide 14: Sine Wave Generator
Waveform dictionary
  512-length arrays
  Respective frequencies
Value loader
  Index: read value
  Different max values

## Slide 15: Sine Wave Generator - frequency
Octave freq. divider
  Save memory space
  Use only Five distinct dictionaries
Physical freq. divider
  Divides oscillator clk into real sine wave clk

## Slide 16: Sine Wave Generator - Structure
Waveform dictionary
Physical freq. divider
Pre-loader
  Input tone (4bit)
  Load dictionary
  Maximum index
  Octave div coefficient
Octave freq. divider
Output value loader
Input:
  Clk: std_logic
  Tone: std_logic_vector (3 downto 0)
Output:
  Wave_out: std_logic_vector(7 downto 0)

## Slide 17: Sine Wave Generator - Structure
Why having two freq. dividers?
Separate the waveform generating process
Easier to create new dictionaries

## Slide 18: PWM Encoder
Nexys 4 DDR has a built-in PWM (Pulse Width Modulation) decoder, which is a low-pass filter.

## Slide 19: PWM Encoder
Input: wave_in : std_logic_vector (7 downto 0)
Calculate Duty Cycle threshold, according to PWM frequency
Counter: smaller than threshold, output ‘1’; else ‘0’
Output: std_logic

## Slide 20: Connecting Components

## Slide 21: Result Demonstration

## Slide 22: Further Development
Better volume/ DA output solution
Beats synthesizer
Synchronization ports
Selectable timbre (square, sine, toothsaw, etc.)
Changeable BPM

## Slide 23: Reference
Frequencies for equal-tempered scale, A4 = 440 Hz http://pages.mtu.edu/~suits/notefreqs.html
Nexys 4 DDR Reference Manual https://reference.digilentinc.com/reference/programmable-logic/nexys-4-ddr/reference-manual
PWM Audio Tutorial using a FPGA https://www.youtube.com/watch?v=4byHVqXD-UI
Class Slides

## Slide 24: Q&A

## Slide 25: GitHub Page
https://github.com/CharlesThaCat/FPGA-Sequencer-and-Synthesizer

## Slide 26: Thank You!